###### CONTENTS

Preparation

Materials	    1

Safety	  4

Tools	  5

Technique	  7

Construction

Profile Pattern	  9

Neck & Tail Blocks	  13

Ribs	  18

Flat Pattern	  20

Bending	  21

Shaping	  25

Back

Assembly Fixture	  29

Assembly	  30

Top Edge	  38

Shaping	  40

Tail Cover Plate	  42

Rib Joint Reinforcement	  43

Neck Joint	  44

Peg Box	  48

Peg Fitting	  52

Neck	  55

Assembly	  56

Shaping	  57

Mounting	  58

Face	  60

Rose Purfling	  67

Roses	  73

Braces	  77

Bridge	  91

Pick Guard	  99

Face Mounting	101

Edge Trim	103

Beard	109

Fingerboard	111

Neck Band	113

Top Nut	115

Strings	117

Mizrabs	121

Finishing	123

General Care	127

Repair		128

Disassembly	129

Poorly Fitting Pegs	130

Split Peg Box	131

Cracks and Crevices	132

Loose Neck	133

Face Repair	134

Delaminated Bridge	135

Worn Fingerboard	136

Refinishing	137

Glossary	138

Drawings

Detail	1	Profile Pattern	  10

Detail	2	End Blocks	  12

Detail	3	Rib Blanks	  19

Detail 	4	Finished Rib	  24

Detail 	5	Back Assembly	  28

Detail 	6	Peg Box Wall	  49

Detail 	7	Peg Box Assembly	  50

Detail	8	Neck	  54

Detail	9	Face Layout	  66

Detail	10	Braces	  80

Detail	11	Bridge	  90

Detail	12	Top Nut	114

DETAIL 5

BACK ASSEMBLY

Clean out the notch carefully with a small chisel all around the edge.

Slice off any remnants of face wood left on the braces with your small chisel. Use both hands to guide the chisel and make small controlled slicing cuts. Always push away from the face edge or parallel to it. Do not push toward the face or you might slip and be sorry. In between the braces the face should cut off clean. The edge of the face can be squared off with your small chisel.